## Slide 1
LNMIIT · ECE · B.Tech Project · 2025–26
From Pipeline Optimization to Deep Learning Acceleration
A Multicore RISC-V FPGA Study
Molik Rajvanshi (23UEC575) · Ujjawal Khatri (23UEC635)
Under Guidance of Dr. Abhishek Sharma
Department of Electronics and Communication Engineering
The LNM Institute of Information Technology, Jaipur
PYNQ-Z2
FPGA Platform
RV32I
ISA
MiBench
Benchmark Suite
5.98×
Max Speedup (8-core)

## Slide 2
Contents
What we'll cover in this presentation
01
Introduction & Research Gap
RISC-V ecosystem, motivation, novel contributions
02
System Architecture
Zynq-7020 multicore design, memory, interconnect
03
Benchmarking Framework
MiBench suite, bare-metal flow, performance metrics
04
Performance Results
Total MIPS, scaling efficiency, resource utilization
05
CNN Inference Application
FruitCNNSmall, int8 quantization, FPGA results
06
Conclusions & Future Work
Key findings, extensions, architectural roadmap

## Slide 3
01
Introduction
Background & Motivation
Lightweight RISC-V soft-cores (PicoRV32, SERV, NEORV32, Ibex, Sodor) have gained substantial research interest in FPGA-based environments due to their open ISA and modular nature.
Most existing research focuses on single-core implementations. Multicore variants exist, but evaluation methodologies differ significantly across studies.
Popular high-performance platforms (e.g., Rocket Chip) target Linux-capable systems leaving a gap for lightweight bare-metal multicore evaluation.
Inconsistent build configs, memory models, and runtime environments make fair cross-study comparison extremely difficult.
Research Gap
→ No unified bare-metal benchmarking framework for lightweight RV32I multicores
→ No hardware-validated fair comparison of pipelined vs multicycle RV32I multicores
→ Inconsistent memory models & runtime environments across published studies
→ Lack of real-world AI workload validation on lightweight FPGA multicore

## Slide 4
Novel Contributions
Seven key research contributions
Multicore Scaling
4-stage RV32I core extended to 2, 4, and 8 cores on PYNQ-Z2 (Zynq-7020)
Fair Arch. Comparison
4-stage pipelined vs 6-stage multicycle under identical runtime conditions
Unified Framework
Bare-metal, mailbox-sync, BRAM-partitioned reproducible benchmark env
MiBench Evaluation
Basicmath, Bitcount, Qsort, Stringsearch, FFT, IFFT, Matmul kernels
Quantitative Analysis
Parallel IPC, MIPS, Speedup, Efficiency via hardware performance counters
Resource Utilization Study
LUT, FF, BRAM, Power for all configs (2/4/8 cores × 2 families)
CNN Inference App
Int8 FruitCNNSmall on 4-core system —> good accuracy, validates embedded AI

## Slide 5
02
System Architecture
Zynq-7020 Multicore RV32I Platform
Zynq PS (Host)
ARM
Cortex-A9
▸ Loads firmware to IMEM
▸ Sends job descriptors
▸ Gathers metrics via mailbox
▸ Runs pooling/FC layers (CNN)
AXI
Interconnect
RV32I Core 0
RV32I Pipeline
Private BRAM Window
Mailbox · Stack · Data
RV32I Core 1
RV32I Pipeline
Private BRAM Window
Mailbox · Stack · Data
RV32I Core N
RV32I Pipeline
Private BRAM Window
128 / 64 / 32 KiB per core
Memory Allocation → N=2: 128 KiB/core · N=4: 64 KiB/core · N=8: 32 KiB/core | Mailbox at 0x2000, Data at 0x2100

## Slide 6
Pipeline Architecture Comparison
4-Stage Pipelined vs 6-Stage Multicycle RV32I
4-Stage Pipelined Core
1. Instruction Fetch (IF)
2. Decode + Register Read (ID)
3. Execute + Memory (EX/MEM)
4. Writeback (WB)
Fmax:
80.77 – 82.19 MHz
Parallel IPC:
Up to 6.16 (8-core FFT)
Max MIPS:
497.3 MIPS (IFFT, 8-core)
Best Kernel:
Matmul (13.59× speedup @8C)
6-Stage Multicycle Core
1. Fetch
2. Decode
3. Execute
4. Memory Access
5. Memory Wait
6. Writeback
Fmax:
72.69 – 80.40 MHz (degrades)
Parallel IPC:
Lower — multicycle stalls
Max MIPS:
319.7 MIPS (Stringsearch)
Bottleneck:
AXI saturation at high N

## Slide 7
03
Benchmarking Framework
Unified bare-metal evaluation environment
Software & Build Flow
▸ No OS / no libc — bare-metal crt0_minimal.S
▸ riscv64-unknown-elf-gcc -march=rv32i -mabi=ilp32-O2
▸ Compile: ELF → BIN → HEX → BRAM load
▸ Tools: AMD Vivado 2022.1 + Vitis 2022.1
MiBench Kernels
● Basicmath
● Bitcount
● Qsort
● Stringsearch
● FFT
● IFFT
● Matmul (custom)
Performance Metrics Used
WALL:
Max cycle count across all cores
Parallel IPC:
Total instructions ÷ WALL
Total MIPS:
Parallel IPC × Fclk (MHz)
Speedup:
vs 2-core baseline (same family)
Efficiency:
÷ (N /2)

## Slide 8
04
Timing Closure Results
Post-implementation Fmax — achieved clock rates used for all measurements
Family | Cores (N) | Treq (ns) | WNS (ns) | Fmax (MHz)
4-Stage (Pipeline) | 2 | 10 | −2.231 | 81.76
4-Stage (Pipeline) | 4 | 10 | −2.167 | 82.19
4-Stage (Pipeline) | 8 | 10 | −2.381 | 80.77
6-Stage (Multicycle) | 2 | 10 | −2.438 | 80.40
6-Stage (Multicycle) | 4 | 10 | −3.037 | 76.71
6-Stage (Multicycle) | 8 | 10 | −3.757 | 72.69
4-Stage Fmax
Stable 80.77 – 82.19 MHz across 2/4/8 cores — minimal WNS variation
6-Stage Fmax
Degrades: 80.40 → 72.69 MHz as N increases — WNS worsens (interconnect timing)

## Slide 9
Total MIPS Comparison
System throughput at achieved clock rates — higher is better
Chart: Total MIPS
| Basicmath | FFT | IFFT | Matmul | Qsort | Stringsearch
4-Stage 2C | 116 | 135.1 | 134.3 | 136 | 93 | 98.5
4-Stage 4C | 233 | 263.9 | 264.1 | 259.6 | 159.4 | 257.6
4-Stage 8C | 420.7 | 496.8 | 497.3 | 488.3 | 214 | 356.9
6-Stage 2C | 49 | 60.8 | 63 | 60.8 | 33.5 | 75.2
6-Stage 4C | 86.8 | 116.5 | 118 | 106.2 | 59.8 | 169.4
6-Stage 8C | 127.2 | 214.7 | 219.3 | 181.3 | 105.5 | 319.7
5.98×
Max Speedup
8-core 4-stage
497 MIPS
Peak Throughput
IFFT, 8-core 4-stage
4-Stage
Consistently Wins
All kernels, all core counts

## Slide 10
Scaling Efficiency
Average efficiency relative to 2-core baseline of same family
Chart: Avg. Efficiency
| 2-core | 4-core | 8-core
4-Stage | 1 | 1.02 | 0.46
6-Stage | 1 | 0.56 | 0.2
Throughput > Frequency
4-stage's higher IPC per cycle beats 6-stage's marginal clock advantage on every workload.
6-Stage Collapses at 8C
AXI interconnect saturation at high core counts severely limits 6-stage parallel efficiency.
Compute-Bound Scales Best
Basicmath, FFT, Matmul show near-linear scaling — zero inter-core comms during compute.
Load Imbalance Issue
Qsort/Stringsearch exhibit sub-linear or degraded scaling due to irregular workload distribution.

## Slide 11
FPGA Resource Utilization & Power
Post-implementation on PYNQ-Z2 (Zynq-7020)
Chart: LUT Usage
| 2-core | 4-core | 8-core
4-Stage | 5921 | 11048 | 28591
6-Stage | 11304 | 22155 | 43731
Chart: Total Power (W)
| 2-core | 4-core | 8-core
4-Stage | 1.446 | 1.475 | 1.63
6-Stage | 1.559 | 1.605 | 1.69
Configuration | LUT | FF | BRAM Blocks | Total Power (W)
4-Stage 8-core | 28,591 | 33,341 | 68 | 1.63 W
6-Stage 8-core | 43,731 | 43,357 | 136 | 1.69 W

## Slide 12
05
CNN Inference Application
FruitCNNSmall — embedded AI on a RISC-V multicore
Why CNN?
Convolution ≡ Matmul (sliding window)
Real-world AI workload validation
Int8 quantization — no FPU needed
Dataset
Fruits-360 · 5 classes · 32×32 RGB
Apple Red 1, Banana, Mango,
Orange, Pomegranate
Model
FruitCNNSmall · 34,357 parameters
float32 accuracy > 98%
Fits in 64 KiB BRAM/core
FruitCNNSmall Layer Architecture
Input
3×32×32
Conv1+ReLU
8×32×32
MaxPool1
8×16×16
Conv2+ReLU
16×16×16
MaxPool2
16×8×8
Flatten
1024
FC1+ReLU
32
FC2 Out
5 classes
4 × RV32I Worker Cores
Conv1: 2 output channels/core · Conv2: 4 output channels/core
Data-parallel MAC — zero inter-core communication during compute
ARM Cortex-A9 (Host)
MaxPool1, MaxPool2, FC1 (int8), FC2 (float), Argmax
Orchestrates load → start → wait → gather pipeline (outputs)

## Slide 13
Int8 Quantization Pipeline
Enabling CNN inference on integer-only RV32I cores
PyTorch Training
FruitCNNSmall in float32
Adam + cross-entropy
>98% test accuracy
→
Activation Calibration
500 balanced images
(100/class)
99.9th pctile + 5% headroom
→
Weight Quantization
Symmetric per-channel
int8 ·
range [−127, 127]
Biases kept as float32
→
C Header Export
Weights → .h arrays
Activation scales exported
Compiled to RV32I binary
→
FPGA Deployment
Worker binary → IMEM
ARM orchestrates pipeline
UART output on PYNQ-Z2
Key Formulas
Weight: s_oc = max|W[oc]| / 127 → W_q[oc] = clamp( round(W[oc] / s_oc), −127, 127 )
Input : x_q = clamp( round(x × 255) − 128, −128, 127 ) | Scales: 0.013972 · 0.070234 · 0.858830

## Slide 14
CNN Classification Results
FPGA int8 inference — all 5 fruit classes correctly classified
Class | FC2 HW Logits | Predicted | ✓?
Apple Red 1 | 3548, −19850, −11432, -14282, −7254 | 0 (Apple) | ✓
Banana 1 | −19686, 27249, 14689, −58571, −3808 | 1 (Banana) | ✓
Mango 1 | −19531, 1256, 10200, −61619, 55 | 2 (Mango) | ✓
Orange 1 | 1177, −43566, −26231, 13483, 2555 | 3 (Orange) | ✓
Pomegranate 1 | −8686, −7359, 57, −18798, 153 | 4 (Pomegranate) | ✓
Good
Accuracy
5 of 5 correct
FPGA
Hardware Verified
UART on PYNQ-Z2
4-Core
RV32I Workers
Conv layers parallelized
Int8
Only — No FPU
Soft-float only for dequant

## Slide 15
Discussion & Key Insights
What the results tell us
01
Throughput Over Frequency
4-stage pipelined design consistently outperforms the 6-stage multicycle architecture across all kernels and all core counts. Optimizing IPC gives greater ROI than maximizing clock speed.
02
Scalability Gap
4-stage scales from 2→8 cores with retained efficiency. 6-stage suffers from AXI bus saturation and BRAM contention at higher N, causing severe parallel efficiency collapse.
03
CNN ≡ Matmul
Convolution layers are structurally identical to Matmul (sliding-window MAC). Matmul achieved 13.59× speedup at 8C —> CNN Conv layers showed similar near-linear scaling across 4 cores.
04
Soft-Float Bottleneck
Without the M extension, integer multiplication requires ~30 cycles. The dequantization step limits CNN efficiency so a fused MAC via DSP48E1 would yield ~10× convolution speedup.

## Slide 16
Towards an AI Accelerator
Proposed architectural extensions
Fused MAC
HW Cost: 1 DSP/core
Expected: ~10× conv speedup
mac rd,rs1,rs2 — single cycle. Aligns with RISC-V P-extension draft.
SIMD Int8 dot4
HW Cost: 4 DSP/core
Expected: +4× throughput
4-way dot product, 16 DSPs total (7.3% of Zynq-7020).
4×4 Systolic Array
HW Cost: 16 DSP shared
Expected: ~63× for Conv2
Dedicated IP block; ARM dispatches via AXI. Google TPU principle at PYNQ scale.
HW ReLU / qReLU
HW Cost: 0 DSP
Expected: 5× activation speed
MUX in writeback stage. BRAM LUT for sigmoid/tanh (LSTM/GRU support).
AXI-DMA Streaming
HW Cost: 0 DSP
Expected: ~30× data load speedup
AXI burst 1–2 GB/s vs 50–100 MB/s PIO. Overlaps data load with ARM compute.
Binary Neural Net
HW Cost: 0 DSP
Expected: 32 MACs per XNOR+popcount
RV32I xor+popcount native. Retrain only, zero hardware change.

## Slide 17
Conclusions
Key findings of this research
01
4-stage outperforms 6-stage on ALL kernels and ALL core counts on the PYNQ-Z2 FPGA.
02
8-core 4-stage achieves up to 5.98× speedup at 28,591 LUTs and 1.63 W total power.
03
6-stage uses 53% more LUTs and 2× more BRAM at 8 cores for inferior performance.
04
FruitCNNSmall on 4-core: good accuracy on 5 fruit classes —> validates embedded AI.
05
Throughput optimization >> clock frequency optimization for FPGA shared-memory multicores.
06
Clear roadmap: fused MAC → SIMD dot4 → systolic array for dedicated AI acceleration.
LNMIIT Jaipur · ECE · BTP 2025–26 · Molik Rajvanshi (23UEC575) · Ujjawal Khatri (23UEC635) · Supervisor: Dr. Abhishek Sharma